## Slide 1: Fingerprint Recognition

## Slide 2: Definition
Biometrics: identifying/authenticating an individual in an automated, reliable and fast way using unique physiological or behavioral characteristics
Physiological: static
morphometric (shape): face
biological: DNA
Behavioral: dynamic
the way we walk, speak, write
https://www.gemalto.com/govt/inspired/biometrics#

## Slide 3: Biometrics Syllabus
PART I BACKGROUND
  Introduction
  Basic pattern recognition aspects
Part II APPLICATIONS
  fingerprints
  facial recognition
  iris scanning
  retina scanning
  hand geometry
  voice verification
  signature verification
  Others (ear biometrics)
  Multi-modal biometrics
Part III Implementation and security issues

## Slide 4: Fingerprint: what
Fingerprint = pattern of flow-like ridges and valleys on the surface of a fingertip
Fingerprint shape is determined during fetal period, depending on the initial conditions of the embryonic mesoderm.
Fingerprints of identical twins are different
No (detail) correlation between prints of different fingers of the same individual
Notes: [Lucian Rila/RHUL]
Fingerprint is the mother biometric and the most widely used biometric. The advent of several inkless fingerprint scanning technologies coupled with the exponential increase in processor performance has taken fingerprint recognition out of the criminal identification applications to several civilian applications such as access control; time and attendance; and computer user login.

## Slide 5: Ancient fingerprints
Notes: From Handbook of Fingerprint Recognition, by Davide Maltoni (Editor), Dario Maio, Anil K. Jain, Salil Prabhakar :
Human fingerprints have been discovered on a large number of archaeological artifacts and historical items (see Figure 1.8 for some examples). Although these findings provide evidence to show that ancient people were aware of the individuality of fingerprints, such awareness does not appear to have any scientific basis.

## Slide 6: Scientific Fingerprint studies
Dermatoglyphics drawn by Grew (1684);
Mayer’s drawings of fingerprints (1788);
Trademark of Thomas Bewick (1806);
The nine patterns illustrated in Purkinje’s thesis (1823);
Sir Francis Galton: minutiae (1892);
Edward Henry: Henry classification (1899)
Notes: It was not until the late sixteenth century that the modern scientific fingerprint technique was first initiated. In 1684, the English plant morphologist, Nehemiah Grew, published the first scientific paper reporting his systematic study on the ridge, furrow, and pore structure in fingerprints

## Slide 7: Fingerprint characteristics
The first legally accepted, readily automated and mature biometric technique
Most understood and studied biometric
Used for a long time : identification studies started late 19th century (FBI 1924: 810K FP cards)
Validity well-established ((FBI,1995): 200 million FP cards (10 fingers))
Daily requests (10K/day) for FPR necessitate automation
AFIS (Automatic Fingerprint Identification Systems) installed (since 1960s) in law enforcing agencies worldwide, continued to IAFIS (Integrated AFIS) maintained by FBI
The success of AFIS led to incorporation in civilian applications
With solid state sensors => incorporation in many applications
Acceptability? Because of association with criminal investigations
https://www.bayometric.com/afis-vs-iafis/

## Slide 8: Fingerprint Recognition System

## Slide 9: Fingerprint Recognition System
https://www.fingerprints.com

## Slide 10: Overall Design of Fingerprint Recognition Systems
Acquisition
Enhancement
Representation/feature extraction
Feature matching

## Slide 11: Fingerprint Acquisition

## Slide 12: Acquisition of Fingerprints
Inked fingerprints (off-line).
  Impression of inked finger on paper.
  Image scanned (using flat bed scanner).
  Cumbersome.
  Infeasible and socially unacceptable for identity verification.
Latent fingerprints on crime scenes.
Live scan (ink-less).
  Image directly obtained without paper impression.

## Slide 13: Fingerprint Examples
Live-scan optical scanner
Live-scan capacitive scanner
Live-scan piezoelectric scanner
Live-scan thermal scanner
Off-line (rolled) inked impression
Latent fingerprint

## Slide 14: Same finger, different FP

## Slide 15: Inked fingerprints

## Slide 16: General structure of FP live-scan device

## Slide 17: Multi-finger and single-finger acquisition

## Slide 18: Rolled versus dab

## Slide 19: Sweeping
Atmel Corp.

## Slide 20: Live-scan Devices: Optical
Optical Frustrated Total Internal Reflection (FTIR)
Ó I/O software
the rays incident at the ridge/glass interface scatter
the rays incident at the valley/glass interface suffers total internal reflection
the reflected rays are collected at the imaging surface
Notes: [Jain & Pankanti:]
Over the last decade, many novel techniques have been developed to acquire fingerprints without the use of ink. These scanners are known as the “livescan” fingerprint scanners. The basic principle in these inkless methods is to sense the ridges and valleys on a finger when the finger is in contact with the surface of the scanner.
The most popular technology to obtain a live-scan fingerprint image is based on the optical frustrated total internal reflection (FTIR) concept [18]. When a finger is placed on one side of a glass platen (prism), ridges of the finger are in contact with the platen, while the valleys of the finger are not in contact with the platen. The rest of the imaging system essentially consists of an assembly of an LED light source and a CCD camera placed on the other side of the glass platen. The laser light source illuminates the glass at a certain angle and the camera is placed such that it can capture the laser light reflected from the glass. The light which is incident on the plate at the glass surface touched by the ridges is randomly scattered while the light incident at the glass surface corresponding to valleys suffers total internal reflection, resulting in a corresponding fingerprint image on the imaging plane of the CCD. An example of live-scan fingerprint is shown in Figure 4 (b). Figure 5 shows a FTIR fingerprint scanner. Typically, an optical live-scan fingerprint scanner images span an area which is approximately

## Slide 21: Live-scan Devices: Optical
+ Oldest and most commonly used (law enforcement)
+ relatively low cost
+ Generally superior quality
+ Potentially larger sensing areas
- Problems with latent fingerprints
+ Cannot be fooled with 2D picture
Bulky (optical path), can not be miniaturized
Ó Biometric Access Corporation

## Slide 22: Live-scan Devices: Optical: smaller alternatives

## Slide 23: Condition-dependent quality

## Slide 24: Live-scan FP acquisition: Differential Capacitance
Notes: [Jain & Pankanti:]
CMOS capacitance [17]: The ridges and valleys of a finger create different charge accumulations when
the finger touches a CMOS chip grid. With suitable electronics, the charge is converted to a pixel value.
Normally at 500 dpi these scanners provide about 0.5” 0.5” of scan area. This can be a problem as the
two images acquired at two different times may have very little overlap. They also tend to be affected by
the skin dryness and wetness. In addition, these devices are sensitive to electrostatic discharge.

## Slide 25: Differential Capacitance
- small surface area: 15x15 mm
+ compact
+ durable and easy to integrate
+ good resolution 500 dpi
+ liveness detection
+ difficult to fool
+ minimal power consumption
+ fast
+ low cost
- sensitive to electrical discharges
Ó Precise Biometrics
300x300, 8-bit

## Slide 26: Live-scan FP acquisition: Ultrasound
Independent of moisture
Independent of dust (cf. infra)
Expensive (2500 Euro)
Bulky still (15x15x20cm)
High Resolution (up to 1000dpi)
3D
Ó Ultra-Scan

## Slide 27: From bulky to under-glass …
Samsung Galaxy S10
@AndroidAuthority

## Slide 28: Ultrasound vs. Optical
Ó Ultra-Scan

## Slide 29: MultiSpectral Fingerprint Acquisition

## Slide 30: 3D Touchless FP acquisition
Improved Quality
Additional Challenge: 3D/2D matching
www.flashscan3d.com
http://www.vis.uky.edu/~realtime3d/Research/Fingerprint.htm
http://www.tbs-biometrics.com

## Slide 31: MorphoWave Desktop

## Slide 32: Touchless (3D) optical scanner
MorphoWave Desktop by IDEMIA scans and processes simultaneously four fingerprints with a single hand movement over its large contactless scanning surface.
This sequence lasting less than a second, MorphoWaveDesktop is then capable of enrolling all 10 fingerprints (2 slaps* and 2 thumbs) in under 5 seconds.
In addition, the 3D technology captures more than just ridges but also surface, shape and curvature of fingers, resulting in a 20%+ higher hit rate than any competing solution (based on an independent study) and a proven compatibility with standard flat and rolled fingerprint databases and AFIS systems.
MorphoWave Desktop copes with wet and dry fingers, mitigates hygiene concerns and is robust against external light and dust.

## Slide 33: Touchless (3D) optical scanner
https://www.idemia.com/morphowave-desktop
https://www.biometricupdate.com/201909/new-ai-engine-boosts-morphowave-compact-biometric-fingerprint-performance

## Slide 34: Live Fingerprints Acquisition Devices
Reference (area, resolution, contrast): inked fingerprints
Optical FTIR (!) (bulky, best quality, large area, expensive)
Differential capacitance (cheap, small, lower Q)
Ultrasound TIR (bulky, quality, small area)
Thermal sensing of temperature differential across ridges and valleys
Non-contact 3-D scanning
See this page (and) for the latest developments and technology comparison
Notes: [Jain & Pankanti:]
CMOS capacitance [17]: The ridges and valleys of a finger create different charge accumulations when
the finger touches a CMOS chip grid. With suitable electronics, the charge is converted to a pixel value.
Normally at 500 dpi these scanners provide about 0.5” 0.5” of scan area. This can be a problem as the
two images acquired at two different times may have very little overlap. They also tend to be affected by
the skin dryness and wetness. In addition, these devices are sensitive to electrostatic discharge.
Thermal [21]: The pyro-electric material in the sensor measures temperature changes as the finger is
swiped over the scanner and produces an image. This technology is claimed to overcome the dry and wet
skin issues in the optical scanners and can sustain higher static discharge. However, the images are not
rich in gray values.
Ultrasound [5]: An ultrasonic beam is scanned across the fingerprint surface to measure the ridge depth
from the reflected signal. Skin conditions such as dry, wet and oil on the skin do not affect the imaging
and the images better reflect the actual ridge topography. However, these units tend to very bulky and
require larger scanning time than the optical scanners.
Recently non-contact [2] fingerprint scanners have been announced to avoid problems related touching a surface for scanning the fingerprint.

## Slide 35: Fingerprint Recognition: Sensors (I)
Capacitive sensor
[FingerTIP™ by Infineon]
Optical fingerprint sensor
[Fingerprint Identification Unit FIU-001/500 by Sony]
Electro-optical sensor
[DELSY® CMOS sensor modul]
© Scarlet Schwiderski-Grosche
Scarlet.Schwiderski-Grosche@rhul.ac.uk
Notes: The sensors by DELSY and Infineon are chip-based.
A picture of an ultrasound fingerprint sensor [by UltraScan] was not available.

## Slide 36: Fingerprint Recognition: Sensors (II)
Thermal sensor
[FingerChip™ by ATMEL (was: Thomson CSF)]
E-Field Sensor
[FingerLoc™ by Authentec]
© Scarlet Schwiderski-Grosche
Scarlet.Schwiderski-Grosche@rhul.ac.uk
Notes: The sensor by Authentec is chip-based.

## Slide 37: Fingerprint Recognition: Integrated Systems (I)
[ID Mouse by Siemens]
[BioMouse™ Plus by American Biometric Company]
© Scarlet Schwiderski-Grosche (Scarlet.Schwiderski-Grosche@rhul.ac.uk)
Physical Access Control System
[BioGate Tower by Bergdata]
Notes: BioMouse™ Plus:
integrated smartcard reader and fingerprint sensor
ID Mouse:
mouse with fingerprint sensor

## Slide 38: Fingerprint Recognition: Integrated Systems (II)
[TravelMate 740 by Compaq und Acer]
Keyboard [G 81-12000
by Cherry]
© Scarlet Schwiderski-Grosche
Scarlet.Schwiderski-Grosche@rhul.ac.uk
Precise 100 PC-Card by Precise Biometrics
Notes: Cherry keyboard:
with integrated smartcard reader and fingerprint sensor

## Slide 39: Advanced fingerprint scanners
Futronic FS60 EBTS/F Certified ID Flat -USB multi finger fingerprint scanner (1900$)
Lumidigm Mercury Series M301 Fingerprint Reader - USB multi-spectral fingerprint scanner (200$)

## Slide 40: Touch ID (Apple)
Capacitance Sensor, 500 DPI

## Slide 41: Fingerprint Representation

## Slide 42: FP Representation
Which machine-readable representation completely captures the
invariant (low intra-class variations) and
discriminatory (high-inter-class variation)
information in a fingerprint image?
Constitutes essence of fingerprint verification system design!
Properties
  Saliency
    contains distinctive information
  Suitability
    Easily extractable
    Compact storage
    Useful for matching

## Slide 43: Structural characteristics: ridges and valleys
Ridge/valley width: 100-300µm

## Slide 44: Representational levels L0-L3

## Slide 45: Representation L0: Entire Gray Scale Profile
Used in optical matching
Verification by template matching
Limitations due to:
  Brightness variations
  Image quality variations
  Scars
  Large global distortions
Representation size is large

## Slide 46: Representation L1: global ridge flow pattern
Only ridge flow and ridge frequency are coded
Singular regions
  Delta (△-shape)
  Loop (⌒-shape)
  Whorl (O-shape)
  Used for classification

## Slide 47: Representations: Entire ridge structure
Image (or graphical coding) of binary image of ridges
Invariant to brightness variations
Sensitive to fingerprint image quality

## Slide 48: Representation L2: Landmark Features - minutiae
local invariant ridge discontinuities, called minutiae
Defined by Sir Francis Galton (1892)!
$ ±150 different types of local ridge structures.

## Slide 49: L2: Landmark Features - minutiae
local ridge discontinuities, called minutiae
$ ±150 different types of local ridge structures.
Difficult to automatically, quickly and reliably extract (too similar and image quality dependent).
Typically: representation based on 2 most prominent:
Ridge endings and ridge bifurcations (are in fact background-foreground duals) or minutiae.

## Slide 50: Minutiae example
Difficult to automatically, quickly and reliably extract (too similar and image quality dependent).
Density: 100/FP but only 10 to 15 needed for matching
In practice only ridge bifurcations and endings are used

## Slide 51: L2 Minutiae Representation
List of minutiae coordinates
Enhanced by tagging each minutiae (or pairs, triplets) with:
  Orientation of the ridge at that minutiae
  Ridge density (# ridges on a line) between each pair of minutiae
Enhanced by global attributes:
  Global orientation of the finger
  Locations of cores or delta’s
  Fingerprint class

## Slide 52: Representation L3 Representations: Pores
Pores are formed where sweat glands in the subcutaneous layer of the skin generate sweat ducts;
these sweat ducts grow through the subcutaneous layer and dermis to the epidermis, where the
open duct on the skin’s surface presents itself as a pore

## Slide 53: Pores
The regularity of their appearance plays a significant part in the uniqueness of pore configurations.
Once these pores form on the ridge, they are fixed at that location.
Pores do not disappear, move or spontaneously generate over time.
Pore sizes: 60-250mm (Ridges: 100-300mm).
Pore density: ±6 pores/mm2.
High resolution sensors needed: 1000dpi (compared to standard 500dpi of FBI’s AFIS specifications).

## Slide 54: Fingerprint Enhancement

## Slide 55: Image Degradation
Non-uniform illumination, dirt, latent prints, scars
Wet finger
Dry finger
Wrinkle

## Slide 56: FP image degradation

## Slide 57: FP image degradation
Types of degradation associated with FP images:
The ridges are not strictly continuous; that is, the ridges have small breaks (gaps).
Parallel ridges are not well separated. This is due to the presence of noise which links parallel ridges, resulting in their poor separation.
Cuts, creases, and bruises on the finger.
This leads to the following problems in minutiae extraction:
a significant number of spurious minutiae are extracted
a large number of genuine minutiae are missed
large errors in the location (position and orientation) of minutiae are introduced.

## Slide 58: FP image enhancement

## Slide 59: Fingerprint Enhancement

## Slide 60: Enhancement: global enhancement
Contrast stretching, Histogram normalization (e.g. standard m, s)

## Slide 61: Enhancement: local adaptive/matched filtering
In contextual filtering, the filter characteristics change according to the local context.
In FP enhancement, the context is defined by the local ridge orientation and local ridge frequency.
An appropriate matched filter that is tuned to the local ridge frequency and orientation can efficiently remove the undesired noise and preserve the true ridge and valley structure.
The intended behaviour :
  provide a low-pass (averaging) effect along the ridge direction with the aim of linking small gaps and filling impurities due to pores or noise;
  perform a bandpass (differentiating) effect in the direction orthogonal to the ridges to increase the discrimination between ridges and valleys and to separate parallel linked ridges.
Using a bank of frequency and orientation selective Gabor filters

## Slide 62: Enhancement: local adaptive filtering
Using a bank of frequency and orientation selective filters

## Slide 63: FP enhancement using bank of Gabor Filters

## Slide 65: Enhancement: examples

## Slide 66: Enhancement: examples

## Slide 67: Fingerprint Compression

## Slide 68: Fingerprint Image Compression
IAFIS (FBI,1995): 200 million FP cards (10 fingers)
Each FP cars scanned at 500dpi: 10MByte
Making 2000 Terabyte in total (1995)
Adding 30.000-50.000 cards A DAY!
Need for compression!
Wavelet Scalar Quantization (WSQ) LOSSY compression (FBI standard for the compression of 500 dpi fingerprint images)

## Slide 69: Fingerprint Image Compression
the central section of a fingerprint image scanned at 500 dpi resolution
the marked portion of the image in a)
the marked portion of the image in a) after the image was compressed using JPEG
the marked portion of the image in a) is shown after the image was compressed using the WSQ compression algorithm.
Both JPEG and WSQ examples used a compression ratio of 1:12.9;
JPEG typically introduces blocky artifacts and obliterates detailed information.
Images courtesy of Chris Brislawn, Los Alamos National Laboratory.

## Slide 70: Fingerprint Image Compression
Original image; file size 589824 bytes

## Slide 71: Fingerprint Image Compression
JPEG image; file size 45853 bytes,compression ratio 12.9.

## Slide 72: Fingerprint Image Compression
WSQ image; file size 45621 bytes, compression ratio 12.9.

## Slide 73: Fingerprint Image Compression
Original image; file size 589824 bytes

## Slide 74: Fingerprint classification

## Slide 75: Fingerprint Classification
Arch
Tented arch
Right loop
Left loop
Whorl
Twin loop
Arch
Tented arch
Right loop
Left loop
Whorl
Twin loop

## Slide 76: Fingerprint Classification
Core = topmost point in innermost ridge
Delta = tri-radial point with three ridges radiating from it

## Slide 77: Fingerprint Classification
Direction field
Smooth Direction field (till classification succeeds)
Locate Singular Points:
    Poincare Index = summing up the changes in direction angle around a closed curve around a point

## Slide 78
Biometrics System Concepts (Course HJ59, K.U.Leuven) – D. Vandermeulen – Fingerprint Recognition

## Slide 79: FP feature extraction

## Slide 80: Representation L1 Ridge (frequency, orientation) extraction

## Slide 81: Orientation Field Estimation
Divide the input fingerprint image into non-overlapping blocks of size WxW (e.g. 16x16)
Compute the gradients Gx and Gy at each pixel in each block
Estimate the (optimal in the least squares sense) local orientation at each pixel [i,j] using the following equations:

## Slide 82: Orientation Field Estimation (2)
Biometrics System Concepts (Course HJ59, K.U.Leuven) – D. Vandermeulen – Fingerprint Recognition
Hierarchical re-estimation based on consistency level of the orientation field in the local neighborhood of a block with the following formula:
D represents the local neighborhood (e.g. 5x5) around the block (i, j); N is the number of blocks within D; q(i’,j’) and q(i,j) are local ridge orientations at blocks (i’,j’) and (i,j), respectively.

## Slide 83: Orientation Field Estimation

## Slide 84: Ridge Detection
Gray level values in ridges attain local maxima along direction normal to the local ridge orientation
  or
Maximum along one of the principal curvatures and zero other principal curvature
ideal
Real fingerprint detail

## Slide 85: Ridge Detection
original
Ridge
Thinned
Cleaned:
remove spikes
join broken ridges

## Slide 86: Representation L2 Minutiae extraction

## Slide 87: Minutiae Detection (1)
Minutiae extracted from ridge image
Trivial if ridge image perfect
Notes: [From the home page of CESENA]
Most automatic systems for fingerprint comparison are based on minutiae matching. Minutiae are essentially terminations and bifurcations of the ridge lines that constitute a fingerprint pattern. Automatic minutiae detection is an extremely critical process, especially in low-quality fingerprints where noise and contrast deficiency can generate pixel configurations similar to minutiae or hide real minutiae. Several approaches to automatic minutiae extraction have been proposed: although rather different from one other, most of these methods transform fingerprint images into binary images through an ad hoc algorithm. The images obtained are submitted to a thinning process which allows for the ridge-line thickness to be reduced to one pixel.

## Slide 88: Minutiae Detection (1)
Ridge image not perfect!
Extraction should degrade gracefully with quality

## Slide 89: Minutiae Detection: Algorithm

## Slide 90: Minutiae and Pores Detection (1a) Gray Scale to Binary Conversion

## Slide 91: Minutiae and Pores Detection (1a) Binary to Skeleton Conversion

## Slide 92: Minutiae and Pores Detection (1a) Skeleton Postprocessing

## Slide 93: Minutiae and Pores Detection (1a) Cleaning and Pore Detection
Biometrics System Concepts (Course HJ59, K.U.Leuven) – D. Vandermeulen – Fingerprint Recognition

## Slide 94: Minutiae and Pores Detection (1a) Results

## Slide 95: Minutiae Detection
Let (x,y) denote a pixel on a thinned ridge
and N0, …, N7 its 8 neighbors

## Slide 96: Minutiae filtering

## Slide 97: Minutiae Detection: result

## Slide 98: Minutiae Quality =f(preprocessing)

## Slide 99: Minutiae Detection (2)
Minutiae detected directly from gray scale images
The basic idea of this method is to follow the ridge lines on the gray-scale image, by "sailing" according to the fingerprint directional image. The algorithm keeps following the ridge lines until they terminate or intersect other ridge lines (minutiae detection).
Notes: [From the home page of CESENA]
In [D. Maio, D. Maltoni, "Direct Gray-Scale Minutiae Detection in Fingerprints", IEEE tPAMI, v. 19, no. 1, 1997] an original technique is proposed, based on ridge-line following, where the minutiae are extracted directly from gray-scale images.
The basic idea of this method is to follow the ridge lines on the gray-scale image, by "sailing" according to the fingerprint directional image. A set of starting points is determined by superimposing a square-meshed grid on the gray-scale image. For each starting point, the algorithm keeps following the ridge lines until they terminate or intersect other ridge lines (minutiae detection). A labeling strategy is adopted to examine each ridge-line only once and locate the intersections between ridge-lines.
The results achieved are compared with those obtained through some methods based on image binarization. In spite of a greater conceptual complexity, the method proposed performs better both in terms of robustness and efficiency (less than 0.2 sec. are necessary to extract all the minutiae from a 256x256 gray-scale image on a Pentium PC).

## Slide 100: Minutiae Detection (2)

## Slide 101: Fingerprint Matching

## Slide 102: Fingerprint Matching

## Slide 103: Fingerprint Matching
Compare test and reference representation
  define/calculate correspondence between features
  define/calculate transformation (rigid/non-rigid)
  define/calculate matching metric
  define a threshold on acceptable matching
based on a model of the expected variations among the representations of mated pairs

## Slide 104: Fingerprint Matching difficulties
Inconsistent mapping of 3-D shape of finger onto 2-D surface of glass platen
  global translation, rotation, scaling (pressure), shear
  local perturbations (small up to only connectivity preserving)
Non-uniform contact (skin dryness, sweat, dirt, humidity): ridges not in contact, valleys in contact, leading to spurious or missing minutiae
Irreproducible contact: injuries changing the ridge structure
Feature extraction artifacts
Additional acquisition artifacts (parallax distortion, previous fingerprint residues)

## Slide 105: Matching Transformations
Euclidean (translation and rotation)
Similarity (Euclidean + scaling)
Affine (Similarity + shear)
Elastic (Affine + local, small, continuous perturbations)
Topological (connectivity preserving)?

## Slide 106: Example

## Slide 107: L2 (minutiae) matching

## Slide 108: Minutiae Matching
Reduces to point pattern matching
define/calculate correspondence
define/calculate transformation (rigid/non-rigid)
define/calculate matching metric
based on a model of the expected variations among the representations of mated pairs

## Slide 109: Minutiae Matching
Reduces to point pattern matching
  define/calculate correspondence
  define/calculate transformation (rigid/non-rigid)
  define/calculate matching metric
based on a model of the expected variations among the representations of mated pairs

## Slide 110: Minutiae Matching
Strategies
  Point Set (with attached attributes) Matching
  Graph-matching
  sub-graph isomorphism
Optimisation
  relaxation
  simulated annealing
  genetic algorithms
Coping with
  poor quality data
  large databases
  geometrical and structural distortion

## Slide 111: Intra-class variations
Displacement: 2 mm ~ 40 pixels at 500 dpi
Rotation: +- 20 degrees
Partial overlap (especially important for small-area sensors
Non-linear distortion (skin plasticity)
Pressure and skin condition (dryness,sweat,dirt, grease, air humidity)
Noise (e.g. residues from previous fingerprints)
Feature extraction errors

## Slide 112: Intra-class variations

## Slide 113: Minutiae Matching
Alignment/Registration
Minutiae Pairing/Correspondence
Matching score computation

## Slide 114: Minutiae Matching

## Slide 115: Minutiae Pairing

## Slide 116: Alignment

## Slide 117: Matching
Find “best” Rigid Transform (θ,Δx,Δy) between minutiae points P and Q
= Point Pattern Matching!

## Slide 118: Alignment
Find “best” Similarity Transform (s,θ,Δx,Δy) between minutiae points P and Q

## Slide 119: Alignment
“Best” = #{overlapping and matching (same orientation) minutiae points} is maximal
Found using generalized Hough Transform
Uses Accumulator Array A with A(k,l,m,n) counting the evidence for Fs,θ,Δx,Δy
For each pair (p,q) ∈ PxQ find all possible transformations Fs,θ,Δx,Δy that map p to q:
∀ (sk,θl): ∃! (Δx,Δy): Fs,θ,Δx,Δy (p) = q
Δx,Δy quantized in bins

## Slide 120: Alignment

## Slide 121: Alignment improvements
Increment neighboring bins as well
Take directions of minutiae into account: increment only if minutiae direction at p when rotated by ql is the same (or about) as the direction in q
Result:

## Slide 122: Minutiae Pairing

## Slide 123: Alignment (2)
Make use of direction and ridge information

## Slide 124: Alignment (2)
Calculate alignment as the similarity transformation that optimally (least squares sense, e.g.) maps the best “correlating” minutiae pair

## Slide 125: Minutiae Matching
Alignment/Registration
Minutiae Pairing/Correspondence
Matching score computation
Errors in localizing minutiae
nonlinear deformations
Elastic matching

## Slide 126: Elastic Matching
Represent minutiae sets as a string in polar co-ordinates (around minutiae pair of maximal consistency): concatenate points in an increasing order of radial angle in polar coordinates
Match the strings with a dynamic programming algorithm, minimizing a cost function such as the “edit” distance C

## Slide 127: String Matching
Biometrics System Concepts (Course HJ59, K.U.Leuven) – D. Vandermeulen – Fingerprint Recognition

## Slide 128: Matching: result

## Slide 129: Matching same FP
Matching score = 49

## Slide 130: Matching different FPs
Matching score = 4

## Slide 131: Minutiae and Pores Representation

## Slide 132: Minutiae and Pores Matching
Maximum correlation
Orientation
Metric = correlation
Metric = #matching pores
=?
Metric = #matching minutiae
=(within position and orientation window)

## Slide 133: L1 feature (ridge) matching

## Slide 134: Feature Space Correlation based matching
Enhancement

## Slide 135: Feature Space Correlation based matching

## Slide 136: Feature Space Correlation based matching

## Slide 137: Feature Space Correlation based matching
Gabor Filtering along 8 orientations
Standard Deviation map
Ridge Feature map

## Slide 138: Multilevel Classification and Matching
1. Determine Fingerprint Class (Arch, Loop, …)
2. Constrain further using ridge density (between cores and deltas)
3. Perform Minutiae based matching

## Slide 139: Individuality of Fingerprints

## Slide 140: FP evaluation

## Slide 141: FVC’2000 Database
Biometrics System Concepts (Course HJ59, K.U.Leuven) – D. Vandermeulen – Fingerprint Recognition

## Slide 142: FVC’2000 Results

## Slide 143: FVC’2002

## Slide 144: FVC’2004
Different (more difficult) databases

## Slide 146: Comparison of Biometrics Technologies

## Slide 147
Notes: Editorial Reviews (from Amazon.com)
Book Info Reference on automatic fingerprint recognition providing in-depth coverage of the most recent advances and practices; including sensing, feature extraction and matching, synthetic fingerprint image generation, indexing, and multimodal systems. For biometric security professionals, researchers, developers, and systems administrators. Book Description With their proven individuality and stability over time, fingerprints continue to be the most widely used physiological characteristic in systems that automatically recognize a person's identity. This comprehensive and authoritative reference, written by leading international researchers, covers all critical aspects of fingerprint security systems and technology. It provides in-depth coverage of the most recent advances and practices: sensing, feature extraction and matching, synthetic fingerprint image generation, indexing, and multimodal systems. The Handbook of Fingerprint Recognition is an absolutely essential resource for all biometric security professionals, researchers, practitioners, developers, and systems administrators.
Features & Benefits:
*Covers the latest research in fingerprint-based recognition algorithms and techniques
*Provides introductory material on all components and modules of a fingerprint recognition system
*Examines design of secure fingerprint systems
*Contains helpful chapter overviews and summaries and consistent notation, for ease of use and accessibility
*Includes a DVD containing both the FVC2002 and FVC2000 fingerprint databases (full versions) and a demo version of SFinGe software (for synthetic fingerprint image generation)
*Integrates numerous supporting graphs, tables, charts, and performance data
*Supplies an extensive annotated bibliography of citations and literature sources

## Slide 148: FP relevance

## Slide 149: Research & Development Projects
Available since 2014
Dedicated sensor
Hot zone under-display
Large area under-display
Full under-display
Capacitive
Optical
Ultrasonic
Optical
Ambition to enter the growing under-display market
Under development
Under development

## Slide 150: Market potential for personal payment devices
Fingerprints™ estimates on shipments based on various industry sources
* Some of these tokens can be used for cryptocurrency, as well as authentication of online payment but more logical access
6-8BN
100MN
40MN
1.5BN
30MN

## Slide 151: Biometric Smartcards – Fingerprints’ strengths
24
Strong experience in high-volume
production
Robust hardware and stable software
Offering biometric performance in a low computing power environment
Ultra-low power consumption
Strong collaboration with smartcard industry leaders

## Slide 152: Market potential for personal Access devices
Fingerprints™ estimates on shipments based on various industry sources
* Used for logical access and access to e.g. cryptocurrency
60MN
225MN
40MN
200MN
50MN
900MN
50MN
60MN
10MN
100MN
7MN
15MN

## Slide 153
34%
33%
32%
32%
29%
29%
28%
28%
Unlocking PC Access car
home time office
Access the Register work Access the Verify Personalize
payments in car settings car
Making payments from PC